## Slide 1: Swing Cam ＆ Half Mount Cam
Your Business Co.,Ltd.
Ver. No.20210701YB
We Your Business Co.,Ltd. has been developing “Swing Cam System”as the third negative angle forming technology, and developed “Half Mount Cam System” since last year. According to these technology, it has achieved to reduce of forming process, saving a cost, improving quality of panel and maintenance by the continuous forming.
We have prepared this technical documents for your initial review of using Swing Cam & Half Mount Cam.
We hope you will find this useful documents.
(Regarding the standard components for Swing Cam & Half Mount Cam, we will separately apply the sheet.)

## Slide 2
Automobile die technology PR material
New technology of die Swing Die＆Half Mount Cam -Contents-
4..2 HOOD OUTER ………………………………………
（Ex.１) ５-combinations …………………………
（Ex.２Ex.３) ３-combinations ……………………
4.3 LIFT GATE OUTER……………………………………
4.4 TRUNK LID OUTER……………………………………
4.5 FR FENDER……………………………………………
（Ex.１) ３-operations ……………………………
（Ex.２） Swing on Swing Cams System …………
（Ex.３） Swing Module(Unit) ………………………
4.6 BODY SIDE OUTER……………………………………
（Ex.１） Drop Swing Cam ………………………
（Ex.２） Arch Swing Cam ………………………
4.7 ROOF …………………………………………………
（Ex.１) ３-operations …………………………
（Ex.２） ……………………………
4.8 BOX SIDE OUTER ……………………………………
⒌ Assembling of the Swing Cam……………………………
5.1 Assembling of the Swing Cam …………………………
5.2 Assembling of the Swing Cam “Easy 3 Steps” …………
⒍ Comparison with other mechanisms ………………………
6.1 Cost Comparison ………………………………………
6.2 Mechanisms Comparison………………………………
⒎ Maintenance ………………………………………………
⒏ Supporting system ………………………………………
⒈ Features of Swing Cam ………………………………………
1.1 Features of Swing Cam ① …………………………………
1.2 Features of Swing Cam ➁ …………………………………
1.3 Comparison with both Swing Cam and holder side ………
1.4 It is possible to reduce the process with combined machining
and continuous machining by Swing Cams Systems ………
1.5 Various Swing Cam Systems ……………………………
① Drop Swing System ……………………
➁ Swing on Swing System …………………
③ Arc Swing System(video ） ………………
④ Half Mount Cam System (video ）…………
⒉ Features of Half Mount Cam ………………………………
2.1 Features of Half Mount Cam ① …………………………
2.2 Features of Half Mount Cam ➁ …………………………
2.3 Air cylinderless mechanism ……………………………
⒊ Making a compact of press die ………………………………
3.1 Making a compact of press die …………………………
3.2 Comparison with Double Cam ①…………………………
3.3 Comparison with Double Cam ➁…………………………
3.4 Comparison with Double Cam ③…………………………
3.5 Comparison with Double Cam ④…………………………
3.6 Comparison with a Counter Cam, a Double Cam
and a Large Cam ………
3.7 Comparison with Rotary Cam ……………………………
⒋ Design Example ……………………………………………
4.1 DOOR OUTER …………………………………………
（Ex.１） ３-operations ………………………………
（Ex.２） ３-operations ………………………………
（Ex.３） ………………………………
23 23
24
25
26
27
27
28
29
30
30
31
32
32
33
34
35
35
36
37
37
38
39
40
3
3
4
5
6
7
7
7
8
8
9
9
10
11
12
12
13
14
15
16
17
18
19
20
20
21
22
-Contents-

## Slide 3: 1.1 Features of Swing Cam①
Contact with 「zero」clearance
It is all machining on flat surface of press die.
It is possible to design the die with a compact.
It is easy for maintenance because stopper plate does not slide.
（１）Compact and simple machining
Integrated structure
（２）Improvement of product quality by high stiffness
（３）Extreme improvement in maintainability
It is possible to be adjusted with shims.
Rotating pivot
“Slide Block”
It is possible to make a forming far from the pivot position.
1．Features of Swing Cam

## Slide 4: 1.2 Features of Swing Cam②
Make the die with a compact
B
B
SEC B-B
It is all machining on flat surface of press die.
1．Features of Swing Cam
Integrated structure
High stiffness
Low cost
With back-up
No sliding portion

## Slide 5: 1.3 Comparison with both Swing Cam and holder side
In case of using Swing Cam,
it is all possible to machine of flat surface on the press die.
1．Features of Swing Cam

## Slide 6: 1.4 It is possible to reduce the process with combined machining and continuous machining by Swing Cams Systems
Large swing direction
Small swing direction
（４）-1 FENDER
（４）-2 DOOR
Cam unit for forming
Cam unit for piercing
Positive Follower System
1．Features of Swing Cam
6/41
（Half Mount Cam system）

## Slide 7
①Drop Swing System
②Swing on Swing System
1.5 Various Swing Cam Systems
1．Features of Swing Cam
7/41
Ex)For BSO, Front Piller etc.
By both the large Swing Cam and small Swing Cam

## Slide 8
③Arc Swing System
④Half Mount Cam System
1．Features of Swing Cam
It is 「zero」clearance at the setting time, but it makes some clearance on the rotating time, which is our Your Business Co.,Ltd. has a patent of the systems.

## Slide 9: 2.1 Features of Half Mount Cam①
A-A
B-B
B→
A→
A→
B→
All flat machining of surface
It is easy to be adjusted.
High Strength bronze with GR
Pre-hardened steel
Contact on Round surface.
2．Features of Half Mount Cam
It is possible to set a position of rotating pivot on the inside of the panel or on the forming side of the panel.

## Slide 10: It is possible to make a structure of the die mounted cam system by a mechanism of the positive return followers.
It is possible to make a structure of larger Swing Cams.(It is available for 4m or more.)
Half mount system is available.
2．Features of Half Mount Cam
2.2 Features of Half Mount Cam②

## Slide 11: 2.3 Air cylinderless mechanism
Half Mount Cam
Lift pin
SEC-A
For example, it is forming structure of narrow area.
2．Features of Half Mount Cam

## Slide 12: 3.1 Making a compact of press die
In case of using Swing Cam
In case of using Double Cam
3．Making a compact of press die
12/41

## Slide 13: 3.2 Comparison with Double Cam①
The edge of the Swing Die
It causes a low productivity.
１、Almost no sliding surface. → Saving for adjustable time.
It is possible to be improved to
a compact structure of press die.
「zero」clearance
２、Compact design.
３、It is possible to be machined with all horizontal and vertical direction.
４、It is possible to be manufactured the integrated punch.
Other steel materials for double cam
（problem on cost and strength）
Double Cam
１、There is many sliding surfaces.
→It is necessary to be adjusted for increasing a time.
２、It makes larger structure of press die.
３、It is difficult to machine.
４、It is necessary to be devided of punch.
５、It is not improved of productivity.
６、There is weak problem on the strength.
3．Making a compact of press die

## Slide 14: 3.3 Comparison with Double Cam②
The Double Cams structure makes the die size become larger.
3．Making a compact of press die

## Slide 15: 3.4 Comparison with Double Cam③
According to devided punch, it decreases the strength of punch.
Since it has to lift a heavy cam driver,
the production speed will slow down
Since it is necessary to devide punch,
the cost of die will increase.
3．Making a compact of press die

## Slide 16: 3.5 Comparison with Double Cam④
Double size of the panel
A
A
Lifting up
SEC A-A
Devided structure
Weak strength
High cost
No back-up
Many sliding area
3．Making a compact of press die

## Slide 17: 3.6 Comparison with a Counter Cam, a Double Cam and a Large Cam
It is increasing the cost of die because of using a Large Cam unit.
Since there are many sliding surfaces, it is not easy for maintenance.
It is necessary to machine the main body side with 5 axes machine.
3．Making a compact of press die

## Slide 18: 3.7 Comparison with Rotary Cam
Pivot position of
Rotary Cam
Pivot position of
Swing Cam
Height at the time of removal
Setting of stopper mechanism
avoiding of rotating.
Forming Load
Swing Cam
Rotary Cam
All around clearance
0.02mm
Contact with 「zero」clearance
Since it is unable to be adjusted of
the clearance for Rotary Cam,
it is necessary to work cladding by welding or remake.
The Rotary Cam is distorted with
cladding by welding & F/H and does not move.
It is possible to make a cladding by welding and F/H.
The Rotary Cams may wear out in production of
around 100,000 units.
Since the Swing Cam keeps zero clearance, there is not weared.
It is very easy to be adjusted with shim up for Swing Cam.
Contact with 「zero」clearance
3．Making a compact of press die

## Slide 19: DOOR OUTER
BOX SIDE OUTER
FR FENDER OUTER
BODY SIDE OUTER
ROOF
4.Design Example
HOOD OUTER
4．Design Example
TRUNK LID OUTER
LIFT GATE OUTER

## Slide 20
The process can be improved by both forming the sash and belt line
at the same time(3 operations).
Whole Door
4.1 DOOR OUTER（Ex.1）
4．Design Example

## Slide 21
A
B
SEC-A
Achieves to 3 operations by processing both cam piercing
and cam flange at the same time with a swing cam.
SEC-B
4．Design Example
[Flange＆Piercing]
[Flange＆Piercing]
[Flange＆Piercing]
4.1 DOOR OUTER（Ex.2）

## Slide 22
4．Design Example
[Cam flange＆Cam piercing]
[Cam flange]
4.1 DOOR OUTER（Ex.3）

## Slide 23
Swing Cams:5-combinations
4.2 HOOD OUTER（Ex.1）
Forming once by Swing Cam
(Improvement of quality, process and no necessary to make the structure of flange lifters.)
4．Design Example

## Slide 24
Swing Cams:3-combinations
4．Design Example
4.2 HOOD OUTER（Ex2、Ex3）

## Slide 25
4.3 LIFT GATE OUTER
4．Design Example

## Slide 26
4.4
TRUNK LID OUTER
4．Design Example

## Slide 27
Fender with 3-operations
4.5 FR FENDER（Ex.1）
4．Design Example

## Slide 28
Swing on Swing Cams System（Large Swing Cam and Small Swing Cam）
4．Design Example
4.5 FR FENDER（Ex.2）

## Slide 29: It is possible to be assembled the Swing Cam or Half Mount Cam as a module of unit.
Unit for wheel arch side
Unit for door side
It is all machining of the assembled surface on the main body,
then it is possible to put Swing Cam on it.
4．Design Example
4.5 FR FENDER（Ex.3） Swing Module(Unit)

## Slide 30
4.6 BODY SIDE OUTER(Ex.1)
（Drop Swing Cam）
4．Design Example

## Slide 31
Arc Swing Cam
4．Design Example
4.6 BODY SIDE OUTER(Ex.2)

## Slide 32
4.7 ROOF（Ex.1）
4．Design Example
3-operations

## Slide 33
A
A
SEC A-A
Hatchback type
Forming Sunroof and beading
4．Design Example
4.7 ROOF（Ex.2）

## Slide 34
Actual results of maximum length 4ｍ
4.8 BOX SIDE OUTER
4．Design Example

## Slide 35: 5.1 Assembling of the Swing Cam
Contact with 「zero」clearance
Contact with 「zero」clearance
It is all adjusted to be flat to the surface of Swing Cam on the area.
It is adjusted to be flat to the bottom surface of Swing Cam.
It is all machining the shape of a flat Swing Cam on the flat surface.
5．Assembling of the Swing Cam

## Slide 36: 5.2 Assembling of the Swing Cam “Easy 3 Steps”
Side clearance
Clearance 0ｍｍ
STEP1
STEP２
Clearance 0~0.05
Target value 0.025
Clearance 0.2~0.15
After adjusting the clearance, it should be checked the operation of the cylinder.
Shape machining
STEP3
Since the Swing Cam is simple structure compared with the other mechanisms, it should be adjusted without a fail before starting of machining shape.
0
0
0
Finally
5．Assembling of the Swing Cam

## Slide 37: 6.1 Cost Comparison
Chart: 
| HALF MOUNT CAM | SWING CAM | DOUBLE CAM | LARGE CAM | ROTARY CAM
Casting Cost | 1 | 1 | 1.3 | 1.5 | 1.5
Components Cost | 0.7 | 1 | 0.75 | 0.9 | 0.5
Assembly Adjustment Cost | 0.6 | 1 | 1.5 | 3 | 2
Machining Cost | 0.5 | 1 | 1.2 | 1.7 | 3.5
6．Comparison with other mechanisms

## Slide 38: 6.2 Mechanisms Comparison
 | Swing Cam Half Mount Cam | Double Cam | Large Cam | Rotary Cam
Total Cost | ○ | △ | × | ×
Die Size | ○ | × | △ | ○
Cam Strength | ○ | × | △ | -
Shortening Process | ○ | × | △ | △
Manufacturing | ○ | △ | × | ××
Maintenance | ○ | △ | × | ×
Product quality | ○ | × | ○ | -
Awareness | △ | ○ | ○ | ○
6．Comparison with other mechanisms

## Slide 39: 7.1 Maintenance
Check the loosening bolt
Do not apply the grease on the contact of 「zero」clearance for the cleaning
１、Cleaning
２、Wipe off the grease on the contact of 「zero」clearance
３、Check the loosening bolt
Check the loosening bolt
Check the loosening bolt
7.Maintenance
Do not apply the grease on the contact of 「zero」clearance for the cleaning

## Slide 40: 8. Supporting system Creating a 3D plan drawing of Swing Cam
File format is dwg.dxf
Solid model of each devided Swing Cam
Data format is STEP, UG, CATIA, etc.
In addition, it is available to convert
to the requested format.
8．Supporting system

## Slide 41
Please contact Your Business Co., Ltd. when you will adopt and learn about Swing Cam.
Swing Cam (registered trademark) is a patented product of Your Business Co., Ltd., and we have obtained and applied for various patents including peripheral patents.
※This content is all effective on dated July 2021 so far.
According to further improvement in product, the specification is subject to change without notice.
Your Business Co.,Ltd.
1466-4 Hino, Hino-city, Tokyo, Japan
191-0012
TEL: +81-42-585-1711
FAX: +81-42-585-1721
http://www.yourb.co.jp/